## Slide 1: TPAC1.2 FDR JC/Feb 27th

## Slide 2: TPAC1.2 FDR Overview
The TPAC design will be re-submitted with two mask changes to fix to key bugs in the design:
  Non-unique address codes in each half of the array
  Oscillation of the in-pixel comparator at very low thresholds
These errors are fixed by changes to
  Mask CS
  Mask M2
Problem reports for TPAC1.1 that will not be addressed in this re-run
  ------------
  Injection from MSO power supply to preAmplifier
    Not easily addressed with mask changes
    Per-pixel masking offers work-around
  ------------
  Injection from DEBUG_HIT_OUT onto DEBUG_RSTVAL1
    Only affects test pixels
    Cosmetic (does not affect in-pixel performance of test pixels)
  Power droop in clock buffer power net for configuration load
    Not easily addressed with mask changes
    Adequate work-around with on-board power module

## Slide 3: Row Addresses
Original TPAC1.0
  Different pixel variants
  Full 168-code row addresses, implemented as two halves
TPAC1.1
  Same pixel variants
  Duplicated half of row addresses
    Ambiguous hit locations!
    Clumsy workaround
TPAC1.2
  Re-instates the unique row-address half removing the duplicated address codes
  implemented by instantiating a pre-existing cell in one half of the array
TPAC1.0
TPAC1.1
TPAC1.2

## Slide 4: Addresses Implementation
Address of each row is set by placing contacts to either VDD or ground
Layout is the same for each row, the contacts are placed by a different cell which makes each row unique
Simple to modify the addressing, by changing CS only
Single bit selects VDD
Single bit selects GND

## Slide 5: Comparator Circuit Analysis
Polarity of injection eliminates coupling between certain nodes
Eventually found that a single parasitic capacitance between comparator output and diode node can cause oscillations at low thresholds
  RCX extracts 30aF between these two nets in the 1.1 pixel design (v small!)
  RCX extracts no parasitics between these two nets in the 1.0 design
  Schematic simulation (no parasitics) with an additional 30aF between the two critical nodes shows oscillations at low thresholds.

## Slide 6: Sanity check
Can 30aF really matter?
  Would not normally consider such tiny parasitics!
  But… diode node is sensitive to induced charge, with a large gain…
Consider a switching 1.8v signal coupling through a 30aF capacitor…
Q = 30 x10-18 * 1.8 = 5.4 x10-17 C
= 337 electrons
Circuit charge gain is ~140uV/e- so… = 47mV signal
!

## Slide 7: TPAC1.0 preShape pixel layout
Comparator output
M1 M2 M3 M4
Comparator output bridges diode node only once, on metal 4 with metal 3 shield.

## Slide 8: TPAC1.1 preShape pixel layout
Comparator output
M1 M2 M3
Comparator output was re-routed in v1.1 over SRAMS but crossing diode node twice
No M2 shield at one crossing creates dominant capacitance between the two nets

## Slide 9: TPAC1.2 preShape pixel layout
Comparator output
M1 M2 M3
Single mask change (M2)
Extended shielding (ground)
RCX tool finds no parasitics between comparator output and diode node 

## Slide 10: Simulation Summary
Design | View | Cpara (HIT DIODE) | Cpara (DIODE GND) | Gain μV/e- | Simulation
Original 1.0 | Schematic | 0 | 14 (est) | 118 | 
 | Extracted (C only) | 0 | 13 | 164 | 
 | Extracted (sel RC) | 0 | 13.3 | 164 | 
Revision 1.1 | Schematic | 0 | 14 (est) | 136 | 
 | Extracted (C only) | 30.25a | 12.1 | 182 | Oscillates at low Vth
 | Extracted (sel RC) | 27.9a | 12.4 | 181 | Oscillates at low Vth
Amended 1.2 | Schematic | 0 | 14 (est) | 160 | 
 | Extracted (C only) | 0 | 12.5 | 180 | 
 | Extracted (sel RC) | 0 | 12.8 | 178 | 

## Slide 11: One more thing…
RCX extraction and simulations report an additional coupling effect in the TPAC1.0 pixel as shown
  This injection has the opposite polarity compared with that discussed so far
  Due to altered signal routing, this is not present in TPAC1.1 or TPAC1.2
  I believe this is an improvement over TPAC1.0 pixels (ie closer to ideal simulations)
    Has not been proven (previously masked by oscillations)
    Injection is not obvious in testing the v1.0 test pixel
300aF

## Slide 12: Comments
Suggested fix adds small additional parasitics to diode node, but acceptable within context of original design
Unsure of reliability of parasitic extraction tools at this precision (10-18)
  what error bars to apply?
Small injection effects are seen in the v1.0 test pixel
  which the RCX tool does not predict
  but the pixel does operate properly

## Slide 13: Measured Injection
Cross check size of injected signal with predicted coupling capacitance
  Charge gain known from marcel’s 55Fe test pixel results
  Can observe signals at two points in analog chain
Induced signal on shaper output
  Varies, in range 1724mV
    Note: Corresponding injection on shaper input will be too small to see on scope (<1mV)
  Applying a gain of 150uV/e-
  Injection varies in range 113160e-
    Right order of magnitude! 

## Slide 14: Other Changes for TPAC1.2
Logo
Mask revision codes
M2
M2 & CS

## Slide 15: GDS DIFF
The TPAC1.1 GDS file submitted on 22/07/08 is compared (XOR) with the new GDS file using calibre
Layer | Name | # XOR geoms | check
34 | CS | 3271 | = 7 + 4 * 816 (revB) (cols) (changes)
42 | M2 | 141179 | = 11 + 3 + 5 * ((168 * 168) + 9 ) (revB) (logo) (changes) (total bulk pixels) (test pix)

## Slide 16: Progress
Top level LVS
Calibre DRC
Compare
Stream Out
Stream In
LVS
Calibre DRC
DPW DRC

## Slide 17: Spare slides
Signals during oscillation
  Triggered by noise
  Oscillation
  Similar scope trace

## Slide 18: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold

## Slide 19: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold

## Slide 20: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold

## Slide 21: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold

## Slide 22: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold
etc…

## Slide 23: Signals
Diode
Preamp out
Shaper out
Comparator

## Slide 24: Signals
Diode
Preamp out
Shaper out
Comparator
Threshold