## Slide 1: TPAC1.1
Jamie Crooks

## Slide 2: TPAC1.1 (honest)

## Slide 3: First Batch
Four boards
  Received 10 at last meeting from Paul
  Tested before bonding
    9 boards operated correctly, testing…
      Operating current
      Board ID
      PCB temperature
      Probed voltages at all power jumpers
      DAC references initial value and read/write
    1 board showed no response from one of the DAC banks
      Returned to IC for investigation
Four chips (12u epi, with DPW)
Three had a power-ground short!
One had sensible power consumption
  Most likely a bonding problem
  New bond program in use for the larger bond pads
  Inspection under microscope shows no obviuos evidence as before, but some occasional material deposits on scribe lane
  Bond program will be modified and a chip reworked to test

## Slide 4: Very First Tests (#32)
Power on
  Sensible current
  Including J1 fitted  promising for the VDD2V5dig bug
SensorLoadV1.1
  See bit errors in columns 2471
  Almost certainly marginal timing on clock edges through up-rated inverter
Monostable test structure
  Working correctly
  Shows that I12IOUTBIAS bug fixed
Chart: Monostable Test Structure
| 2500 | 2400 | 2300 | 2200 | 2100 | 2000 | 1900 | 1800 | 1700 | 1600 | 1500 | 1400 | 1300 | 1200 | 1100 | 900 | 700 | 500 | 300
 | 722 | 614 | 522 | 460 | 400 | 358 | 322 | 290 | 263 | 236 | 216 | 201 | 188 | 179 | 175 | 207 | 268 | 366 | 580

## Slide 5: TPAC1.0
Jamie Crooks
On behalf of Barnaby Levin & Michael Lynch

## Slide 6: Summer Students
Bulk pixel scans
  Perl scripts automate…
    “runStart” commands
    Movement of X/Y stage
    Laser parameters
  Root programs automate
    Function fitting to threshold scans
    Data plotting
Analog test-pixel scans
  Labview automates
    Acquisition of measurements from LeCroy scope
    Movement of X/Y stage
    Laser parameters
  Root programs automate
    Data plotting
Laser reliability
Fully documented on “Spider Wiki”
  Results
  Flow charts
  Software documentation
  Source code

## Slide 7: Test pixel scans
2x2um laser
2um steps
Two runs
  Something crashed
  Laser intensity different after restart
    Hence the different peaks!
  Will repeat
    This sensor
    Non-DPW sensor
    5um EPI sensor

## Slide 8: Laser uniformity
If laser is turned off/on…
If connection between labview and laser is broken/remade…
Over long periods (weekend)…
1: Stop Any Software Running The Laser
2: Turn Laser Off At Key
3: Wait For Short Period
4: Turn Laser On At Key
5: Wait For Short Period
6: Fire Laser From Control Box With Desired Settings For Short Period
7: Stop Firing
8: Start Labview, (Will not connect first time)
9: Restart Labview (Software should now be working)
10: Fire Laser From Computer
11: Wait For a Short Period
12: Take Measurements
1: Stop Any Software Running The Laser
2: Turn Laser Off At Key
3: Wait For Short Period
4: Turn Laser On At Key
5: Wait For Short Period
6: Fire Laser From Control Box With Desired Settings For Short Period
7: Stop Firing
8: Start Labview, (Will not connect first time)
9: Fire Laser From Control Box With Desired Settings For Short Period
10: Stop Firing
11: Restart Labview (Software should now be working)
12: Fire Laser From Computer
13: Wait For a Short Period
14: Take Measurements
Some improvement made by manually firing the laser before re-connecting with labview
Needs more understanding (/fixing?)
Any absolute calibration method must eliminate non-uniformity of this kind